## Slide 1: Intelligent Test Pattern Optimization
Digital Circuit Testing | Capstone Project

## Slide 2: Problem and Objectives
Generate test patterns and target faults
Rank/select patterns to detect faults efficiently
Compare AI-assisted selection with basic and random strategies
Measure coverage, number of patterns, and runtime

## Slide 3: Circuit Under Test
Inputs: a, b, c, d; outputs: y0, y1, y2
n1 = a XOR b; n2 = c AND d
n3 = a OR c; n4 = NOT(b AND d)
y0 = n1 XOR n2; y1 = n3 AND n4; y2 = y0 OR y1

## Slide 4: Fault Model and Patterns
7 nodes × SA0/SA1 = 14 target faults
A fault is detected if any output changes
Exhaustive generation: 2⁴ = 16 input patterns
Detection matrix stores detected/not-detected for each pattern/fault

## Slide 5: AI Ranking
Features: input bits, number of ones, transitions, balanced-bit flag
Target: number of faults detected per pattern
RandomForestRegressor with 250 trees
Greedy coverage selector avoids redundant patterns

## Slide 6: Results
AI: 4 patterns, 92.9% coverage
Basic: 4 patterns, 92.9% coverage
Random mean: 3.77 patterns, 94.9% mean coverage
See results/strategy_comparison.csv for the full data. AI is not guaranteed to outperform baselines.

## Slide 7: Tools and Reproducibility
Python, NumPy, Pandas, scikit-learn
Install: python -m pip install -r requirements.txt
Run: python src/main.py
Fixed random seed; 100 random-order trials

## Slide 8: Limitations and Future Work
Small educational circuit; not industrial ATPG
Only single stuck-at faults
Extend to larger benchmarks and Verilog simulation
Add structural features and compare with ATPG methods

## Slide 9: Conclusion
Complete pipeline: patterns → fault simulation → ranking → selection
Report actual fault coverage rather than only AI scores
Code, datasets, report, and presentation are included